## Slide 1
Power Flow in a Transmission Line System
This presentation will discuss:
Thevenin’s Theorem
Maximum Power Transfer
Conservation of Energy
Forward and Reflected Power
Matched and mismatched lines
VSWR, Return Loss and Reflection Coefficient
Time delay
Impedance Matching
Component Failures due to mismatches
Transmitter protection and turn-down

## Slide 2: Thevenin’s Theorem and Conservation of Energy: Maximum power transfer occurs when the Load impedance is equal to the complex conjugate of the Thevenin equivalent Source Impedance For resistive terminations, maximum power transfer occurs when the source resistance equals the load resistance, also: Load Power = Total Input Power – Losses (PL = Pt - Ploss), Load Power is power delivered to Load, and in terms of Pf and Pr: Load Power = Forward Power - Reflected Power - Losses (PL = Pf – Pr – Ploss) Both equations describe Conservation of Energy After steady state is achieved; Load Power = Tot Power (PL = Pt) for a lossless transmission line

## Slide 3: For a coaxial line, Z0 represents the Thevenin equivalent impedance of the coaxial cable then: Maximum power transfer occurs when ZL also = Z0 as a pure resistor This is defined as a “Matched System”, with 0 reflected power Unless otherwise noted: This Forum will use PeP as the reference Power

## Slide 4: Some definitions and derivations: Special case – Lossless line: Forward Power – Power injected into the transmission line: Power, P = vrms2/R, or, in terms of peak voltage, Power, P = Vp2 / (2xR), then Forward Power for sine wave excitation is: Pf = Vpf2 / (2xZ0) where Z0 = Line Impedance, Vpf is forward peak voltage, and: Reflected Power – Power rejected by the load and reflected back toward the source: Pr = Vpr2 / (2xZ0)

## Slide 5: Rearrange terms, solve for peak voltages: _________ Vpf = √(2 x Pf x Z0) __________ Vpr = √(2 x Pr x Z0)

## Slide 6: Load Power: Power delivered to the load: For a resistive load: PL = VpL2 / (2xRL) Solving for Peak Load voltage: _________ VpL = √(2 x PL x RL) Vpf, Vpr and VpL are peak voltages, and RL is in Ohms

## Slide 7: Define magnitude of Reflection coefficient |Γ|, Return Loss, and VSWR: |Γ| is the ratio of reflected voltage divided by forward voltage (Some technical references use ρ instead of Γ) |Γ| = Vpr / Vpf --- Vpr = |Γ| x Vpf Return Loss in dB = -20 x LOG (|Γ|) >>> S11 Define Voltage Standing Wave Ratio (VSWR): VSWR = ( 1 + |Γ| ) / ( 1 – |Γ| ) If Vpr = Vpf then |Γ| = 1, and VSWR = ∞

## Slide 8: Rearrange terms and solve for |Γ|: |Γ| = (VSWR -1 ) / (VSWR + 1) If |Γ| = 1, Forward Power equals Reflected Power, vf = vr and No power is delivered to the load; all of the power is re-sent back to the source

## Slide 9: VSWR also represents the ratio of maximum and minimum peak voltages on a transmission line: VSWR = vmax / vmin where: vmax = Vpf + |Γ| x Vpf vmin = Vpf - |Γ| x Vpf Vmax = Vpf ( 1 + |Γ|) Vmin = Vpf ( 1 - |Γ|)

## Slide 10: Solving for VSWR and Return Loss in terms of power: Since vr = |Γ| x Vf, it can be shown that: Pr = |Γ|2 x Pf Return Loss in dB can also be calculated as: RLdB = 10 x LOG (Pf / Pr), also ______ |Γ| = √ (Pr / Pf) then: |Γ|2 = Pr / Pf which yields: Pr = |Γ|2 x Pf Also: ______ _______ VSWR = [1 + √ (Pr / Pf ) ] / [ 1 - √ (Pr / Pf ) ] Also, for a resistive load (antenna at or very close to resonance): VSWR = RL / Z0, or Z0 / RL whichever gives a result greater than 1

## Slide 11: Define Forward Transmission Loss in dB (LF dB) and Efficiency Loss in dB: Lf dB = -10 x LOG ( 1 -|Γ|2 ) -> S21 Lf dB is also call efficiency loss in dB (ζ dB): S21 -> Insertion Loss or Transducer gain ζ dB = -10 x LOG (PL / Pt) or ζ dB = 10 x LOG (Pt / PL)

## Slide 12: Examples: A 50 ohm transmitter connected to a lossless 50 ohm line, terminated in a resistive load, no matching device (Xmt power = 100 watts)
Xmtter
100 w
Directional
Wattmeter
Lossless line
Load
Pf
Pr
PL

## Slide 13: Example 1: RL = 50 ohms (matched) Since there is no matching device (tuner), Transmitter output (Pt = Pf), and, Pr = 0, since there is no reflected power: PL = Pt = Pf = 100 watts VSWR = 1.0, |Γ| = 0 Solve for Vpf VpL, and Vpr _________ ___________ Vpf = √ (Pf x 2xZ0) = √ (100 x 2x50) = 100 v, peak; VpL = Vpf = 100 volts peak Vpr = 0

## Slide 14: Directional Wattmeter reads 100 watts Forward power and 0 watts Reflected power, indicating the matched condition. Example 2: Load Resistance = 100 ohms, or 25 ohms, no matching device Determine VSWR, Vpf Vpr VpL |Γ| Pf RLdB Pr and PL

## Slide 15: For RL = 100 ohms: VSWR = 100 / 50 = 2.0 For RL = 25 ohms: VSWR = 50 / 25 = 2.0 Note that both loads produce the same VSWR Since VSWR for both loads is the same, |Γ| for both loads must also be the same. But what is the difference?

## Slide 16: Difference is not in the magnitude of the reflection, but in the phase of the reflection. If RL > Z0, Vpr is in phase with Vpf and adds to vpf, VpL = Vpf + Vpr If RL < Z0, Vpr is out of phase with Vpf and subtracts from Vpf, VpL = Vpf - Vpr VpL is measured at the load; Vpr propagates back to the source and either adds or subtracts from vf depending on distance on the line from load

## Slide 17: For either RL = 100 ohms or 25 ohms, assuming a constant power system of 100 watts: ____________ Vpf = √ (100 x 2x50 ) = 100 v |Γ| = (VSWR – 1) / (VSWR + 1) |Γ| = (2 – 1) / ( 2 + 1) = 0.3333 Vr = |Γ| x Vf = 0.3333 x 100 = 33.333 volts RLdB = - 20 x LOG (33.333 / 100) = 9.54 dB ….. (S11) Pf = 100 watts (assuming that Xmtr is capable of delivering full power into this mismatch) Pr = |Γ|2 x 100 = 11.1 watts PL = Pf – Pr = 100 – 11.1 = 88.9 w

## Slide 18: Does this violate Conservation of Energy? How can two different loads yield the same delivered power? Validity check -> RL = 100 ohms Vf is in phase with vr then load voltage adds VL= Vf + Vr VL = 100 + 33.333 = 133.333 volts Since Power = Vp2 / (2xR), then, Load Power, PL = VpL2 / (2xRL) PL = (133.33)2 / 200 = 88.9 watts which agrees with the previous result

## Slide 19: Validity check when RL = 25 ohms: Since RL < Z0, vpr is out of phase with vpf and subtracts: VL = Vf – Vr VL = 100 – 33.33 = 66.67 volts PL = (66.67)2 / (2x25) = 88.9 watts, which also agrees with previous Therefore, conservation of energy is not violated, and is validated for any equal VSWR condition.

## Slide 20: Solving for Forward transmission loss (Efficiency Loss dB or S21) S21 = 10 x LOG (Pt / PL) S21 = 10 x LOG (100 / 88.9) S21 = 0.52 dB Therefore, there is a 0.52 dB loss for an ideal lossless transmission line terminated in a VSWR of 2, with no matching device.

## Slide 21: Using min / max voltages to compute VSWR: Vmax = Vpf + Vpr = 100 + 33.333 vmax = 133.333 volts vmin = Vpf – Vpr vmin = 100 -33.333 vmin = 66.67 volts VSWR = vmax / vmin VSWR = 133.333 / 66.67 = 2

## Slide 22: Calculate Return Loss dB using Forward and Reflected Power: RLdB = 10 x LOG (100 / 11.1) = 9.54 dB which agrees with the previous result that used forward and reflected voltages

## Slide 23: Interesting case: RL = 0 (short circuit) Pt = 100 w No antenna tuner and Lossless Line As before, Pt = 100 w, Pf = Pt, and Vpf = 100 volts Since the load is a short circuit, VpL = 0 ….. Where did the voltage go? Does this violate conservation of energy? VSWR = Z0 / RL = ∞ >>> No power is delivered to Load since VSWR = ∞, |Γ| = 1 and Vr = Vf But ZL < Z0, then Vpr is out of phase with Vpf at the load

## Slide 24: Two voltages appear at the load, Vf, and Vr, that are equal in amplitude and opposite in phase vf vr + = _____________ vL = 0 volts They cancel and produce 0 volts (flat line) You, the observer, sees 0 volts, and assumes there is no load voltage, since you cannot separate vf and vr vr propagates back to the source generating reflected power Conservation of energy is not violated

## Slide 25: Some important points to remember: 1. Forward power and Reflected power values are constant no matter position on a lossless transmission line 2. Vf and Vr are vector quantities in magnitude and phase, and can only be separately measured by using a directional coupler. The actual voltages and currents along a mismatched transmission line will vary depending on VSWR, position and / or line length.

## Slide 26: 3. For a perfectly matched lossless line, Vpf = VpL and is constant no matter line length or position 4. VSWR = 1, Pf = PL Pr = 0, and |Γ| = 0 for a perfectly matched lossless line 5. System efficiency, (ζ), can be calculated from: ζ = {PL / Pt} x 100% 6. Efficiency Loss in dB (LdB) is calculated from: -10 x LOG (ζ /100) and is the same as Forward transmission loss (S21), in dB 7. When an antenna tuner is used, Reflected Power is not lost power, and may contribute to power delivered to the load (Will be discussed later in this presentation)

## Slide 27: 8. For a lossless line, VSWR is constant, and does not change with line length. 9. Effective radiated power from an antenna is the product of power delivered to the antenna, (Load Power), times the isotropic antenna gain, where antenna gain (directivity), is expressed as a power ratio ERP = PL x Ga If antenna gain is in dB, (dBi), then ERP = PL x 10(dBi/10)

## Slide 28: Transmission Line Time delay Fundamental wave equation: d = c0 x t (Distance = rate x time) d =Distance of travel in meters c0 = speed of light in free space, ≈ (3 x 108 meters / sec) t = time in seconds Solving for t, and redefining t as time delay (td): td= d / c0 in free space but waves travel slower in cable due to the velocity factor (VF) Then, in cable, substituting cable length in feet as distance, (Lfeet = d, 1 meter ≈ 3.2808 feet) One way Time delay in nano seconds: td nsec = 1.0157 x Lfeet / VF

## Slide 29: Two special cases: 1. Line length an integer number of half waves long, (Integers, 1, 2, 3, 4, etc.): Since free space wavelength, λ0 = c0 / FHz Using feet and MHz, λ0 feet = 984.3 / FMHz In transmission lines, velocity of propagation is reduced by velocity factor, VF, then: λcable = 984.3 x VF / FMHz, and ½ λcable= 492.15 x VF / ( FMHz) Conditions on a lossless transmission line repeat every integer number of half wave lengths of line; lines that are an integer number of half waves long are called Impedance Repeaters

## Slide 30: 2. Odd number of Quarter wave lengths of line, (N =1, 3, 5, 7, etc): ¼ λ cable = 246.08 x VF / FMHz Conditions on the line invert every odd number of quarter waves of line. For example, Vmax becomes Vmin and vice-versa every odd multiple of quarter wave lengths along the line. Therefore line lengths that are an odd numbers of quarter wavelengths long are called Impedance Inverters.

## Slide 31: Power Flow Analysis in Systems using an Antenna Tuner, and lossy transmission line Analysis is more complex since Forward and Reflected Voltages are modified by the impedance matching action of the tuner, and also, Vpf and Vpr voltages are attenuated as they travel along the line. Results are facilitated by using a spreadsheet

## Slide 32: Definition of Impedance Matching: Impedance matching device satisfies 2 conditions: 1. Transform output voltage and current (vout and iout to new values of vin and iin 2. Satisfy condition #1, above, in a lossless fashion so that Pin = Pout Input Impedance, Zin = vin / iin Output Impedance, Zout = vout / iout For resistive sources and loads: Pin = vin x iin Pout = vout x iout If matching circuit is ideal and has no loss: vin x iin = vout x iout

## Slide 33: Antenna System for Analysis: Note location of Directional Wattmeter, after the Antenna Tuner:
Xmtter
100 w
Directional
Wattmeter
Lossy line
Load (Ant)
Pf
Pr
PL
Antenna
Tuner
Failure?
Failure?

## Slide 34: Examine what happens in a transmission line when the Antenna Tuner is adjusted for a perfect match Spreadsheet will look for possible failures in the Antenna Tuner and / or Antenna system due to mismatches in the system, and calculate power flow within the antenna / transmission line system. The antenna system includes: Baluns / Ununs Traps / Loading Coils Stubs / Phasing lines Etc.

## Slide 35: Case studies: For all 7 cases: Tuner / Antenna rated at 300 watts, 100 watt transmitter (no turn-down) 1. VSWR = 1, ≈ Lossless Line 2. VSWR = 1, 50 feet of line, 0.6 dB loss / 100 ft 3. VSWR = 2, same line as 2 4. VSWR = 3, same line as 2 5. VSWR = 10, same line as 2 6. VSWR = 20, same line as 2 7. VSWR = 20 ≈ Lossless line

## Slide 36: Final Comments: Why do some transmitters need to reduce output power when loaded in a relatively minor mismatch? For example a VSWR of 2 produces only about 11% reflected power, yet most manufacturers favor turn-down starting at about 2.0 VSWR, some even at a VSWR of 1.5 Are transmitter designs so marginal that they cannot tolerate 11% or less reflected energy?

## Slide 37: Consider a VSWR of 2, which corresponds to a |Γ| of 0.3333; where maximum voltage or current in this system is 33.33% higher than nominal rated. So failures could result from excess voltage or current, and not necessarily only due to reflected power. Vacuum tube final amplifiers are more tolerant of mismatch, and are usually more rugged. Regardless, tubes operate at high B+ voltages and other components in the amplifier may operate at high RF current levels; where a 33% increase could be damaging. Thus, most tube amplifiers still require some type of protection. Also, tube circuits are high impedance output stages that require a form of matching to drive low impedance loads. In other words, the antenna tuner is built in to the amplifier as part of the design; they can adjust the output matching network (PI network), to accommodate a up to ≈ 10 to 1 VSWR.

## Slide 38: Solid state output amplifiers are usually broadband devices that are designed to provide power into a rated load. They do not have a tuned matching network built into the output, and can be modeled as current sources. These amplifiers are designed to operate within a required “Load Line” range, for rated output, rated efficiency, and dissipated power. Outside of this Load Line region, efficiency deteriorates rapidly, and device dissipation quickly rises, and could over heat the solid state junction ( in less than 1 msec) So, solid state amplifiers not only have to contend with excess voltage and/or current due to mismatches, but also have to contend with efficiency degradation. Thus, power turn down may be necessary to protect the devices.

## Slide 39: Questions or Comments?

## Slide 40: Email me if you want a copy of this presentation or spreadsheet: dmkozma@optonline.net Thank you and hope to see you on the air. Mike WY2U